Schematic for a minimum 1-Wire raingauge. It will work with Dallas Semiconductor software, but not with software from Texas Weather Instruments, or Point Six. CR1 across the bus is to protect against undershoots. CR2, shown as a dual-diode, can be separate single Schottky diodes. It functions as an OR gate to supply power from the 3V Lithium battery to the DS2423 counter whenever the bus is off to maintain the rainfall count.The value of C1 is not critical, but it should be very low leakage. R1 pulls the counter inputs low to maximize noise rejection. SW1, the reed switch, is to be mounted on the raingauge and operated by a permanent magnet. The mechanics and calibration can be challenging.